## Slide 1
CSE208 · DIGITAL LOGIC DESIGN LABORATORY · CLASS 04
Subtractors: Half & Full
Borrowing with logic gates — the same XOR, a different second output
Munzer Mahmood
Lecturer, Department of Computer Science and Engineering
Presidency University

## Slide 2
Recap · Class 03
Where We Are
CSE208 · Digital Logic Design Laboratory · Class 04
2
Last class you learned
Binary addition: 1 + 1 = 102 → Sum 0, Carry 1
Half adder: S = A ⊕ B, C = AB
Full adder: S = A ⊕ B ⊕ Cin
Cout = AB + Cin(A ⊕ B)
Full adder = 2 half adders + 1 OR gate
Last class
Gates → binary addition
Today
Gates → binary subtraction
Almost the same circuit — watch carefully what changes.
Notes: Recap the adder. Stress that the Difference output will turn out to be the same XOR as the Sum.

## Slide 3
Today's Learning Objectives
CSE208 · Digital Logic Design Laboratory · Class 04
3
By the end of today's laboratory, you should be able to:
1
Apply the rules of binary subtraction, including the borrow.
2
Define a half subtractor and derive its truth table.
3
Use minterms and the SOP method to derive its Difference and Borrow.
4
Explain why a half subtractor is not enough for multi-bit subtraction.
5
Define a full subtractor and derive its Difference and Borrow-out expressions.
6
Build a full subtractor using two half subtractors and an OR gate.
7
Verify subtractors using a simulator or the 7486, 7408, 7432 and 7404 ICs.

## Slide 4
Motivation
Why Do We Need Subtractors?
CSE208 · Digital Logic Design Laboratory · Class 04
4
Subtraction is the second arithmetic operation every processor must perform — and it is where the idea of a borrow comes from:
Comparison
A − B shows which value is larger
Counting down
Timers, loop counters, countdowns
Address arithmetic
Offsets and differences of addresses
Subtractor
ALU
CPU
Computer
Build a circuit that subtracts two single bits — then copy it for every bit.
Real processors often subtract by adding the 2's complement — but the borrow is what we learn here.
Notes: Mention 2's complement: real ALUs often subtract by adding. The dedicated subtractor is how we learn the borrow.

## Slide 5
The four cases
Binary Subtraction Rules
CSE208 · Digital Logic Design Laboratory · Class 04
5
Subtracting two 1-bit numbers has only four cases:
0 − 0 = 0
Borrow = 0
Difference = 0
102 − 1 = 1
(0 − 1, after borrowing)
Borrow = 1
Difference = 1
1 − 0 = 1
Borrow = 0
Difference = 1
1 − 1 = 0
Borrow = 0
Difference = 0
Two outputs
Every column produces a Difference (D) and a Borrow (Bout) taken from the next column.
Why borrow?
0 − 1 is impossible in one column, so we borrow 2 from the left: 102 − 1 = 1.
Two inputs, two outputs — that is exactly a half subtractor.
Notes: Stress the second case: 0 minus 1 cannot be done in one column, so we borrow from the next column to the left.

## Slide 6
Why one circuit is not enough
Subtracting Multi-bit Numbers
CSE208 · Digital Logic Design Laboratory · Class 04
6
Borrow
A
− B
Diff
1
1
0
1
1
0
1
1
0
0
1
0
1
(11)
(6)
(5)
2 bits in
3 bits in
1
Rightmost column: A0 − B0 — only 2 bits, nothing is borrowed yet.
2
Every other column: Ai − Bi − borrow-in — 3 bits.
3
A column that cannot subtract borrows from the column to its left.
2 inputs ⇒ Half Subtractor 3 inputs ⇒ Full Subtractor
Here only bit 2 borrows — but any column might.
Notes: Work the example column by column. Only bit 2 generates a borrow, and bit 3 has to subtract it.

## Slide 7
Topic 1 · Half subtractor
The Half Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
7
Definition
A half subtractor is a combinational circuit that subtracts two 1-bit inputs, B from A, and produces two outputs: a Difference (D) and a Borrow (Bout).
Inputs: A (minuend), B (subtrahend)
Outputs: D, Bout
Bout = 1 means we had to borrow from the next column
Why “half”?
It subtracts only two bits — there is no input for a borrow from a previous column.
Order matters: A − B is not the same as B − A.

## Slide 8
Topic 1 · Half subtractor
Half Subtractor — Truth Table
CSE208 · Digital Logic Design Laboratory · Class 04
8
A
B
Bout
D
0
0
0
0
0
1
1
1
1
0
0
1
1
1
0
0
Only row 01 needs a borrow
Look at column D
D = 1 when the inputs are different → XOR
Look at column Bout
Bout = 1 only when A = 0 and B = 1 → NOT + AND
Half subtractor = one XOR + one AND + one NOT
The Difference is the same XOR as the adder's Sum.
Notes: Compare with the half adder: the D column is identical to S, only the second output differs.

## Slide 9
Technique · SOP
Deriving the Expressions
CSE208 · Digital Logic Design Laboratory · Class 04
9
Use the Sum of Products (SOP) method:
1
Write the minterm of every row where the output is 1.
2
OR those minterms together.
3
Simplify and recognise the gate.
D = 1 in rows 01 and 10
Bout = 1 only in row 01
Compare with the half adder: C = AB, but Bout = A̅B — the minuend is inverted.
One inverter is the whole difference between adding and subtracting.
Notes: Same SOP method as the adder. The only new thing is the complemented literal in the borrow term.

## Slide 10
Topic 1 · Half subtractor
Half Subtractor — Logic Circuit
CSE208 · Digital Logic Design Laboratory · Class 04
10
Boolean expressions
In the laboratory
One gate of the 7486 (XOR), one of the 7408 (AND) and one of the 7404 (NOT) on input A.
Gates used: 1 XOR + 1 AND + 1 NOT.

## Slide 11
Worked example
Let's Trace It: Half Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
11
Given the half subtractor circuit, suppose:
1
XOR:
2
NOT + AND:
3
Check:
Try it yourself
Repeat the trace for A = 1, B = 1. What are D and Bout?

## Slide 12
Topic 1 · Half subtractor
Limitation of the Half Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
12
A half subtractor has only 2 inputs.
From the 2nd column on we must handle 3 bits: Ai, Bi and the borrow-in.
So, it works only for the least significant bit.
Add a third input for the incoming borrow → the Full Subtractor
One missing wire is the whole difference.
Notes: Same argument as the half adder: from the second column on, three bits arrive.

## Slide 13
Topic 2 · Full subtractor
The Full Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
13
Definition
A full subtractor subtracts three 1-bit inputs — it computes A − B − Bin and produces a Difference (D) and a borrow-out (Bout).
Inputs: A, B, Bin (3 bits)
Outputs: D, Bout
Smallest result: 0 − 1 − 1 = −2, so one borrow is always enough
The chain
The Bout of one column becomes the Bin of the next column.
Three bits in, two bits out — enough for every column.

## Slide 14
Topic 2 · Full subtractor
Full Subtractor — Truth Table
CSE208 · Digital Logic Design Laboratory · Class 04
14
A
B
Bin
Result
Bout
D
0
0
0
0
0
0
0
0
1
−1
1
1
0
1
0
−1
1
1
0
1
1
−2
1
0
1
0
0
1
0
1
1
0
1
0
0
0
1
1
0
0
0
0
1
1
1
−1
1
1
Result = A − B − Bin; a negative result needs a borrow
Look at column D
D = 1 when an odd number of inputs are 1 — exactly like the adder's Sum.
Look at column Bout
Bout = 1 whenever A − B − Bin goes below zero.
D = Σm(1, 2, 4, 7)
Bout = Σm(1, 2, 3, 7)
Eight rows — verify every one of them in the lab.
Notes: Read the Result column: a negative value means a borrow, and D is that value plus 2.

## Slide 15
Topic 2 · Full subtractor
Full Subtractor — Deriving the Difference
CSE208 · Digital Logic Design Laboratory · Class 04
15
minterms 1, 2, 4, 7
group by A
XOR and XNOR
the XOR pattern again
Exactly the same expression as the full adder's Sum.
Adding and subtracting differ only in the second output.
Notes: Identical algebra to the full adder's Sum, because the minterms are the same.

## Slide 16
Topic 2 · K-map
Can We Simplify D?
CSE208 · Digital Logic Design Laboratory · Class 04
16
The 1s form a checkerboard — no two 1s are adjacent.
No group of 2 or 4 is possible, so the SOP cannot be simplified.
Use XOR gates instead of four 3-literal AND terms.
A checkerboard K-map is the signature of an XOR function.
The same map we drew for the adder's Sum.

## Slide 17
Topic 2 · K-map
Deriving Bout with a K-map
CSE208 · Digital Logic Design Laboratory · Class 04
17
m1, m3
→
A̅Bin
m2, m3
→
A̅B
m3, m7
→
BBin
Bout = A̅B + A̅Bin + BBin
Compare with the adder
Cout = AB + ACin + BCin. The subtractor is the same shape with A inverted.
Notes: m3 is shared by all three groups. Note every group sits in the A = 0 row except the one with m7.

## Slide 18
Topic 2 · Full subtractor
Another Form of Bout
CSE208 · Digital Logic Design Laboratory · Class 04
18
minterms 1, 2, 3, 7
group the terms
complement law
Form 1 (from the K-map)
1 NOT + 3 AND + 1 three-input OR
Form 2 (reuse the XOR)
2 NOT + 2 AND + 1 OR
A ⊕ B is already built for the Difference — so reuse its complement.
Notes: This second form reuses A XOR B from the Difference, which leads to the two-half-subtractor design.

## Slide 19
Topic 2 · Full subtractor
Full Subtractor — Logic Circuit (SOP Form)
CSE208 · Digital Logic Design Laboratory · Class 04
19
Boolean expressions
In the laboratory
One inverter makes A̅, which feeds two of the AND gates.
Gates used: 2 XOR + 1 NOT + 3 AND + 1 three-input OR.

## Slide 20
Topic 2 · Full subtractor
Full Subtractor from Two Half Subtractors
CSE208 · Digital Logic Design Laboratory · Class 04
20
1
Half Subtractor 1 handles A − B → P = A ⊕ B, G = A̅B
2
Half Subtractor 2 handles P − Bin → D = P ⊕ Bin, X = P̅·Bin
3
OR gate combines the two borrows → Bout = G + X
Full Subtractor = 2 Half Subtractors + 1 OR gate
Notes: G and X can never both be 1, so a plain OR is enough to combine the two borrows.

## Slide 21
Topic 2 · Full subtractor
Full Subtractor — Gate-Level Circuit
CSE208 · Digital Logic Design Laboratory · Class 04
21
Gates used: 2 XOR + 2 NOT + 2 AND + 1 OR
Think
Can G and X both be 1 at the same time? (No — so the OR never has to add two borrows.)

## Slide 22
Worked example
Let's Trace It: Full Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
22
Suppose:
1
HS 1:
2
HS 2:
3
OR:
4
Check:
Try it yourself
Trace A = 0, B = 1, Bin = 1. What are D and Bout?

## Slide 23
Summary
Half Subtractor vs Full Subtractor
CSE208 · Digital Logic Design Laboratory · Class 04
23
Feature
Half Subtractor
Full Subtractor
Inputs
2 (A, B)
3 (A, B, Bin)
Outputs
D, Bout
D, Bout
Difference
A ⊕ B
A ⊕ B ⊕ Bin
Borrow
A̅B
A̅B + Bin(A ⊕ B)′
Basic gates
1 XOR + 1 AND + 1 NOT
2 XOR + 2 AND + 2 NOT + 1 OR
Used for
The LSB only
Every bit position
A full subtractor with Bin = 0 behaves exactly like a half subtractor.

## Slide 24
Summary
Adder vs Subtractor — Side by Side
CSE208 · Digital Logic Design Laboratory · Class 04
24
Adder
Subtractor
Operation
A + B (+ Cin)
A − B (− Bin)
First output
S = A ⊕ B ⊕ Cin
D = A ⊕ B ⊕ Bin
Second output (half)
C = AB
Bout = A̅B
Second output (full)
AB + Cin(A ⊕ B)
A̅B + Bin(A ⊕ B)′
Extra gate needed
—
NOT on A, and on P
Built from
2 half adders + OR
2 half subtractors + OR
Same XOR, same structure — only the inverters are new.
Notes: The punchline of the class: invert the minuend and an adder becomes a subtractor.

## Slide 25
In the lab
Laboratory ICs
CSE208 · Digital Logic Design Laboratory · Class 04
25
7486
Quad 2-input XOR
7408
Quad 2-input AND
7432
Quad 2-input OR
7404
Hex inverter (NOT)
Important
The 7404 is different: it has six 1-input gates, so the pins run input–output–input–output. VCC is still pin 14 and GND still pin 7.
New chip today: the 7404 inverter is what turns an adder into a subtractor.

## Slide 26
Logisim Evolution
Circuit Simulation
CSE208 · Digital Logic Design Laboratory · Class 04
26
Build the half subtractor once, then reuse it twice.
1
Create a circuit named HalfSubtractor.
2
Place inputs A, B and outputs D, Bout.
3
Wire one XOR, one NOT and one AND; test all 4 rows.
4
Create a second circuit, FullSubtractor.
5
Place two HalfSubtractor sub-circuits and one OR.
6
Test all 8 input combinations.
7
Compare with the truth table.
One block, used twice
Keep the adder file open — the two circuits differ by one inverter.

## Slide 27
Quiz
Quick Check #1
CSE208 · Digital Logic Design Laboratory · Class 04
27
How many inputs and outputs does a half subtractor have?
Hint: which bits does it subtract, and what does it produce?

## Slide 28
Quiz
Quick Check #1
CSE208 · Digital Logic Design Laboratory · Class 04
27
How many inputs and outputs does a half subtractor have?
Hint: which bits does it subtract, and what does it produce?
2 in, 2 out

## Slide 29
Quiz
Quick Check #2
CSE208 · Digital Logic Design Laboratory · Class 04
28
A full subtractor has A = 0, B = 1, Bin = 1. What are D and Bout?
Hint: 0 − 1 − 1 = −2, so borrow and add 2.

## Slide 30
Quiz
Quick Check #2
CSE208 · Digital Logic Design Laboratory · Class 04
28
A full subtractor has A = 0, B = 1, Bin = 1. What are D and Bout?
Hint: 0 − 1 − 1 = −2, so borrow and add 2.
D = 0, Bout = 1

## Slide 31
Quiz
Quick Check #3
CSE208 · Digital Logic Design Laboratory · Class 04
29
Which gate turns a half adder into a half subtractor?
1
AND
2
OR
3
NOT
4
NAND

## Slide 32
Quiz
Quick Check #3
CSE208 · Digital Logic Design Laboratory · Class 04
29
Which gate turns a half adder into a half subtractor?
1
AND
2
OR
3
NOT
4
NAND
NOT

## Slide 33
Quiz
Quick Check #4
CSE208 · Digital Logic Design Laboratory · Class 04
30
How many half subtractors (plus one OR gate) make a full subtractor?
Hint: one for A − B, then one for the borrow-in …

## Slide 34
Quiz
Quick Check #4
CSE208 · Digital Logic Design Laboratory · Class 04
30
How many half subtractors (plus one OR gate) make a full subtractor?
Hint: one for A − B, then one for the borrow-in …
2

## Slide 35
Class 05
What Comes Next?
CSE208 · Digital Logic Design Laboratory · Class 04
31
Next class
Karnaugh Map Based Combinational Design — a picture instead of algebra.
We used a K-map twice already, for Cout and for Bout. Next class we make it the main tool:
Group the 1s
Adjacent cells merge and drop a variable
Read it off
Each group becomes one product term
Build it
Fewer gates for the same function
Same circuits, fewer gates — simplification is a design skill.

## Slide 36
Summary
Today's Takeaways
CSE208 · Digital Logic Design Laboratory · Class 04
32
1
Binary subtraction: 0 − 1 needs a borrow from the next column.
2
Half subtractor: D = A ⊕ B, Bout = A̅B.
3
The Difference is the same XOR as the adder's Sum.
4
A half subtractor has no borrow-in, so it fits only the LSB.
5
Full subtractor: D = A ⊕ B ⊕ Bin.
6
Bout = A̅B + A̅Bin + BBin = A̅B + Bin(A ⊕ B)′.
7
Full subtractor = 2 half subtractors + 1 OR gate.

## Slide 37
Self-check
Before You Leave
CSE208 · Digital Logic Design Laboratory · Class 04
33
You should be able to answer:
1
What is the difference between a half and a full subtractor?
2
Why is the Difference the same as the adder's Sum?
3
Write the complete truth table of a full subtractor.
4
Derive Bout using a K-map.
5
How do you build a full subtractor from two half subtractors?
6
Which ICs do you need to build a full subtractor in the lab?

## Slide 38
Assessment
Lab Task — Experiment 04
CSE208 · Digital Logic Design Laboratory · Class 04
34
Implementation of Half Subtractor and Full Subtractor
Construct the following circuits and verify every row of the truth table.
Part A — Half Subtractor
One XOR + one NOT + one AND
ICs: 7486, 7404, 7408
Verify all 4 rows
Part B — Full Subtractor
Two half subtractors + one OR gate
ICs: 7486, 7404, 7408, 7432
Verify all 8 rows
Submit:
1
Circuit diagrams
2
Truth tables
3
Boolean expressions & K-maps
4
Experimental observations
5
Short conclusion

## Slide 39
One Inverter Makes the Difference
1
Half subtractor — 2 bits in, Difference and Borrow out
2
Full subtractor — 3 bits in, handles the borrow from the last column
3
Two half subtractors + OR — the standard full subtractor
4
The Difference is the adder's Sum — only the borrow is new
NEXT CLASS
Karnaugh Maps
Group the 1s and read off the simplest expression.
Questions?