## Slide 1
CSE207 · DIGITAL LOGIC DESIGN · LECTURE 01
Welcome to the World of 0s and 1s
Switching circuits, truth tables, logic gates, Boolean algebra and simplification
Munzer Mahmood
Lecturer, Department of Computer Science and Engineering
Presidency University
Notes: Welcome students. Today we start from the very bottom: how a simple switch becomes a 0 or a 1, and how we describe and simplify circuits built from them.

## Slide 2
What is Digital Logic Design?
CSE207 · Digital Logic Design · Lecture 01
2
Digital Logic Design is about building circuits that work with only two values:
0 and 1
You'll find digital logic inside:
Computers and smartphones
Calculators and digital watches
Traffic lights and elevators
Washing machines and microwaves
Analog Any value in a range, like a dimmer knob
Digital Only 0 or 1, like a light switch
Notes: Analog signals can take any value in a range (a dimmer). Digital signals take only two values (a light switch). Digital is used because two values are easy to tell apart even with noise, and easy to build with transistors.

## Slide 3
Today's Roadmap
CSE207 · Digital Logic Design · Lecture 01
3
1
Switching Circuits
How a simple switch stands for a 0 or a 1
2
Truth Tables
Writing down every possible input and its output
3
Logic Gates
AND, OR, NOT and their friends
4
Boolean Algebra
The math rules for 0 and 1
5
Simplification
Making circuits smaller and cheaper
Each topic builds on the one before it.
Notes: Five topics. Each one uses the one before it.

## Slide 4
1
Topic 1 of 5 · Switching Circuits
A Switch Is a Bit
CSE207 · Digital Logic Design · Lecture 01
4
The simplest digital circuit is a battery, a switch and a lamp.
Switch OPEN → 0
No current flows · Lamp OFF
Switch CLOSED → 1
Current flows · Lamp ON
Inside every chip are billions of tiny switches called transistors, each one ON (1) or OFF (0).
Notes: Simplest digital circuit: battery, switch, lamp. Open switch means no current, lamp off, we call it 0. Closed switch means current flows, lamp on, we call it 1. A transistor is just an electronic switch.

## Slide 5
1
Topic 1 of 5 · Switching Circuits
Series = AND, Parallel = OR
CSE207 · Digital Logic Design · Lecture 01
5
Series connection
Lamp is ON only if A AND B are both closed
Y = A · B
Parallel connection
Lamp is ON if A OR B (or both) is closed
Y = A + B
Notes: Series: current must pass through A and then B, so both must be closed. That is AND. Parallel: current can take either path, so one closed switch is enough. That is OR. In the picture, the parallel circuit has A open and B closed, and the lamp is still on.

## Slide 6
2
Topic 2 of 5 · Truth Tables
Truth Table: List Every Possible Case
CSE207 · Digital Logic Design · Lecture 01
6
A truth table shows the output for every combination of inputs. Nothing is left out.
2
rows
1 input
4
rows
2 inputs
8
rows
3 inputs
Rule: n inputs → 2n rows
Example: the series (AND) circuit
A | B | Lamp Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
The lamp is ON (1) only in the last row, when both switches are closed.
Notes: A truth table has one row for every input combination. Each input can be 0 or 1, so every new input doubles the rows: 2, 4, 8, 16. Example: the series (AND) circuit.

## Slide 7
2
Topic 2 of 5 · Truth Tables
Writing a Truth Table Without Missing a Row
CSE207 · Digital Logic Design · Lecture 01
7
Row | A | B | C
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
1
Count the rows: 3 inputs → 23 = 8 rows
2
Column C (last): flip every row → 0 1 0 1 …
3
Column B: flip every 2 rows → 0 0 1 1 …
4
Column A (first): flip every 4 rows → 0000 1111
Shortcut: the rows are just 0 to 7 counted in binary!
Notes: Trick for filling inputs: the last column flips every row, the next every 2 rows, the first every 4 rows. It is the same as counting 0 to 7 in binary.

## Slide 8
3
Topic 3 of 5 · Logic Gates
Logic Gates: The Basic Three
CSE207 · Digital Logic Design · Lecture 01
8
A logic gate is a tiny circuit: it takes 0/1 inputs and gives one 0/1 output.
NOT Y = A'
Flips the input
A | Y
0 | 1
1 | 0
AND Y = A · B
1 only when ALL inputs are 1
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR Y = A + B
1 when ANY input is 1
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Notes: A logic gate is a small circuit that follows one fixed rule. AND = all inputs must be 1. OR = at least one input is 1. NOT = flips the input.

## Slide 9
3
Topic 3 of 5 · Logic Gates
Four More Gates You'll Use Often
CSE207 · Digital Logic Design · Lecture 01
9
NAND Y = (A · B)'
AND + NOT. Output is 0 only when both inputs are 1.
Outputs (00, 01, 10, 11): 1 1 1 0
NOR Y = (A + B)'
OR + NOT. Output is 1 only when both inputs are 0.
Outputs (00, 01, 10, 11): 1 0 0 0
XOR Y = A ⊕ B
Output is 1 when the inputs are different.
Outputs (00, 01, 10, 11): 0 1 1 0
XNOR Y = (A ⊕ B)'
Output is 1 when the inputs are the same.
Outputs (00, 01, 10, 11): 1 0 0 1
Notes: NAND is AND followed by NOT; NOR is OR followed by NOT (the small bubble means NOT). XOR: inputs different gives 1. XNOR: inputs same gives 1. Output strings are for inputs 00, 01, 10, 11.

## Slide 10
3
Topic 3 of 5 · Logic Gates
NAND & NOR: The Universal Gates
CSE207 · Digital Logic Design · Lecture 01
10
A universal gate can build ANY other gate using only copies of itself.
Why only these two?
AND and OR can't flip a value (no NOT)
NOT can't combine two inputs
NAND and NOR do both: combine AND flip
XOR is not universal. It can't build AND or OR.
Building the basic gates
Gate | Only NAND | Only NOR
NOT A | (A · A)' | (A + A)'
A · B | ((A · B)')' | (A' + B')'
A + B | (A' · B')' | ((A + B)')'
Example: to get NOT from a NAND, connect A to both of its inputs.
Any ' inside the table is itself made from the same gate.
Notes: Universal means you can build NOT, AND and OR, and so every circuit, using only that one gate type. NOT from NAND: tie both inputs together, (A·A)' = A'. AND from NAND: a NAND followed by a NAND-made NOT. OR from NAND: invert both inputs first, (A'·B')' = A + B by De Morgan. NOR is the mirror image. XOR is not universal: it can make NOT but never AND or OR.

## Slide 11
4
Topic 4 of 5 · Boolean Algebra
Boolean Algebra: Math with 0 and 1
CSE207 · Digital Logic Design · Lecture 01
11
Every variable is either 0 or 1. There are only three operations:
A · B
AND (like ×)
1 · 1 = 1, everything else is 0
A + B
OR (like +)
0 + 0 = 0, everything else is 1
Careful: 1 + 1 = 1, not 2!
A'
NOT (complement)
0' = 1 and 1' = 0 (also written Ā)
Order of operations
NOT → AND → OR
(just like × before +)
Example: Y = A'·B + C with A = 0, B = 1, C = 0
Y = 1 · 1 + 0 = 1 + 0 = 1
Notes: Boolean algebra is ordinary-looking algebra where every variable is 0 or 1. Important difference: in OR, 1 + 1 = 1, not 2. Precedence: NOT first, then AND, then OR.

## Slide 12
4
Topic 4 of 5 · Boolean Algebra
Basic Laws of Boolean Algebra
CSE207 · Digital Logic Design · Lecture 01
12
Law | OR form | AND form
Identity | A + 0 = A | A · 1 = A
Null | A + 1 = 1 | A · 0 = 0
Idempotent | A + A = A | A · A = A
Complement | A + A' = 1 | A · A' = 0
Involution | (A')' = A | 
Commutative | A + B = B + A | A · B = B · A
Associative | A + (B + C) = (A + B) + C | A(BC) = (AB)C
Distributive | A + BC = (A + B)(A + C) | A(B + C) = AB + AC
Absorption | A + AB = A | A(A + B) = A
Check any law
Put A = 0, then A = 1. If both sides always match, the law is true.
Duality
Swap + with · and 0 with 1 to get each law's partner.
A + 0 = A ↔ A · 1 = A
Notes: Most laws come in pairs: an OR form and an AND form. Note the second distributive law, A + BC = (A + B)(A + C), which is NOT true in normal math but is true in Boolean algebra. Students can check any law by trying A = 0 and A = 1.

## Slide 13
4
Topic 4 of 5 · Boolean Algebra
De Morgan's Theorem
CSE207 · Digital Logic Design · Lecture 01
13
(A + B)' = A' · B'
NOT of an OR = AND of the NOTs
(A · B)' = A' + B'
NOT of an AND = OR of the NOTs
Proof with a truth table: (A · B)' = A' + B'
A | B | A · B | (A · B)' | A' | B' | A' + B'
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0
Memory trick
Break the bar, change the sign.
Put the NOT on each variable, and swap AND ↔ OR.
Notes: Two rules for pushing a NOT inside brackets. The truth table proves the second one: the highlighted columns (A·B)' and A' + B' are identical in every row.

## Slide 14
5
Topic 5 of 5 · Simplification
Why Simplify a Boolean Function?
CSE207 · Digital Logic Design · Lecture 01
14
The same logic can be written the long way or the short way. Shorter means fewer gates.
BEFORE
F = AB + AB'
4 gates
2 AND · 1 OR · 1 NOT
AFTER
F = A
0 gates
Just a wire from A!
Cheaper
fewer parts
Faster
signals pass fewer gates
Cooler
uses less power
Notes: Every symbol in an expression becomes real hardware. AB + AB' needs two ANDs, one NOT (for B') and one OR. After simplification it is just A: a plain wire. Next slide shows how.

## Slide 15
5
Topic 5 of 5 · Simplification
Simplification: Step by Step
CSE207 · Digital Logic Design · Lecture 01
15
Example 1
F = AB + AB'
= A(B + B')
Distributive law
= A · 1
Complement law
F = A
Identity law
Example 2
F = A + A'B
= (A + A')(A + B)
Distributive law
= 1 · (A + B)
Complement law
F = A + B
Identity law
Example 3
F = (A + B)(A + B')
= A + BB'
Distributive law
= A + 0
Complement law
F = A
Identity law
Tip: look for a variable next to its complement (like B and B'). They often cancel out.
Notes: All three follow the same pattern: use the distributive law to group, the complement law to make a 1 or a 0, then the identity law to finish. Example 2: A + A'B = (A + A')(A + B) uses the OR form of the distributive law.

## Slide 16
5
Topic 5 of 5 · Simplification
Practice: Simplify These
Simplify each expression. Name the law you use at every step.
P1
F = A(A' + B)
P2
F = AB + A'B
P3
F = (AB)' + A
P4
F = (A + B')' + A'B'
P5
F = A'B' + A'B + AB
P6
F = ABC + ABC' + AB'C
CSE207 · Digital Logic Design · Lecture 01
16
Notes: In-class practice, easiest first. Solve these on the board with the students.

## Slide 17
5
Topic 5 of 5 · Simplification
Homework: Simplification
Simplify each expression. Show every step and write the law used.
H1
F = A + A'B'
H2
F = (A + B)(A + C)
H3
F = A'B + AB' + AB
H4
F = (A'B')' (A + B')
H5
F = ABC + AB'C + A'BC
H6
F = (A + B + C)(A + B + C') (A + B')
CSE207 · Digital Logic Design · Lecture 01
17
Notes: Homework problems.

## Slide 18
Quick Check
CSE207 · Digital Logic Design · Lecture 01
18
1
Two switches are in parallel. A = 0 and B = 0. Is the lamp ON or OFF?
2
How many rows does a truth table with 4 inputs need?
3
Which gate gives 1 only when its two inputs are different?
4
Simplify: F = A + AB
Notes: Answers: 1) OFF, both paths are open (0 + 0 = 0). 2) 2^4 = 16 rows. 3) XOR. 4) F = A + AB = A(1 + B) = A · 1 = A (Absorption law).

## Slide 19
Today's Takeaways
1
A switch is a bit: open = 0, closed = 1.
2
A truth table lists all 2n input cases.
3
Gates: AND = all, OR = any, NOT = flip. NAND & NOR are universal.
4
Boolean laws let us rewrite expressions safely.
5
Simpler expression → fewer gates → cheaper, faster circuit.
NEXT LECTURE
Canonical & Standard Forms
Karnaugh Map (K-map) Method
A faster, visual way to simplify Boolean functions.
Questions?
Notes: Recap the five ideas. Next class: canonical and standard forms, then Karnaugh maps.